## Slide 1: Project report - bearing
Group2
Bing-Hong Hong
Hsin-Ting Chou
Chih-Hao Chiang
Shao-Tse Chien

## Slide 2: Outline
Background
Flow chart
Bearing dataset
Feature extraction
Feature selection
Cross-validation
Model training
conclusion

## Slide 3: Background

## Slide 4: Introduction
Bearing is a machine element that can reduce sliding friction.
It can improve the efficiency, durability and performance.
Review of Techniques for Bearings & Gearbox Diagnostics.pdf

## Slide 5: Problem Statement
The goal of this project is to diagnose the specific failure modes when bearing is known degraded.
SKF 32208 tapered roller bearing
  Pitch Diameter (D) = 60mm
  Roller Diameter (d) = 10mm
  Number of Roller (n) = 17
  Contact Angle (Φ) = 14.04
  Rotating speed of inner race () = 800 rpm
  Rotating speed of outer race ( = 0 rpm
https://www.kugellager-express.de/tapered-ball-bearing-32208-40x80x24-75-mm

## Slide 6: Cases
Healthy
Roller (Ball) damage
Inner race defect
Outer race defect
Inner + Roller
Outer + Roller
Inner + Outer
Inner + Outer + Roller
https://slideplayer.com/slide/5780979/

## Slide 7: Parameters
Ball Passing Frequency Outer Race (BPFO)
Ball Passing Frequency Inner Race (BPFI)
Fundamental Train Frequency (FTF)
Ball Spin Frequency (BSF)
D = pitch dia; d = ball dia; = contact angle;
n = no. of balls
Review of Techniques for Bearings & Gearbox Diagnostics.pdf

## Slide 8: Situations
Bearing Defect
  Frequency of Outer Ring Defect (FORD)
  Frequency of Inner Ring Defect (FIRD)
  Frequency of Ball Defect (FBD)
  http://www1.udel.edu/present/Becky/bearing/
https://gfycat.com/lividsarcasticguineapig

## Slide 9: Situations(cont’d)

## Slide 10: Solutions
Time Waveform Analysis
Frequency Spectral Analysis
High Frequency Detection (HFD)
Stress Wave Analysis or Spike Energy
Enveloping

## Slide 11: Enveloping
Enveloping is a technique that can extract the modulating signal from an amplitude modulated signal by Hilber transform.
http://www.power-mi.com/content/demodulation-or-envelope-analysis

## Slide 12: Feature of bearing fault
Rolling element bearing fault frequencies are generated when a bearing begins to fatigue.
Time domain statistical parameters, such as Root Mean Square Amplitude (RMS), are also calculated from vibration data and monitored for a significant increase in magnitude.
These fault or defect frequencies are calculated using bearing geometry and speed.

## Slide 13: Feature of bearing fault(cont’d)
Manually observing the spectrum for increases throughout testing was not feasible due to the fact that these tests often ran unattended. For this reason, a technique was developed to trend the defect frequencies on-line. Using the defect frequencies BPFI, BPFO, BSF, FTF as indexes for the frequency domain data.

## Slide 14: Assumptions Made in Bearing Fault Frequencies
1. All balls/rollers are equal in diameter
2. There in pure rolling contact between balls, inner race and outer race.
3. There is no slipping between the shaft and the bearing
4. Outer race is stationary and inner race rotates
Bearing faults create a series of impacts which are amplified by resonances: bearing, sensors, structure etc

## Slide 15: Decision Fusion Analysis
Reference: Dempsey, Paula J., Gary Kreider, and Thomas Fichter. "Tapered Roller Bearing Damage Detection
Using Decision Fusion Analysis." (2006).

## Slide 16: Flow chart

## Slide 17: Flow chart
Data
Preprocessing
Feature extraction
Feature selection
SOM
GMM+EM
SVM
SOM-MQE
DNN

## Slide 18: Bearing dataset

## Slide 19: Bearing dataset
training data is given with 2048 tests, as well as labels for all the 2048 tests. Labels are numbers from 1 to 8, and each class has 256 samples, corresponding with normal, roller, inner race, outer race, inner race & roller, inner race & outer race, outer & inner race & roller, and outer race & roller.

## Slide 20: Feature extraction
Time domain: Mean、Variance、Skewness、Kurtosis、Entropy、Peak-to-peak、RMS
Frequency domain: BSF、BPFI、BPFO

## Slide 21: Feature selection

## Slide 22: Fisher score

## Slide 23: Feature visualization(cont’d)

## Slide 24: Feature visualization(cont’d)

## Slide 25: Feature visualization(cont’d)

## Slide 26: K-fold Cross validation(K=4)

## Slide 27: Model training
SOM
SOM-MQE
Support vector machine(SVM)
GMM+EM
Deep neural network(DNN)

## Slide 28: SOM

## Slide 29: SOM U-Matrix

## Slide 30: SOM-MQE
validation 1: 0.8457
validation 2: 0.9082
validation 3: 0.8828
validation 4: 0.8867
Total ACC : 0.8809

## Slide 31: Support Vector Machine (SVM)

## Slide 32: Support Vector Machine (SVM)
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 63 | 1 | 0 | 0 | 0 | 0 | 0 | 98.4% 1.6%
0 | 0 | 60 | 4 | 0 | 0 | 0 | 0 | 93.7% 0%
0 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 64 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 64 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 0 | 64 | 100% 0%
100% 0% | 100% 0% | 98.3% 1.7% | 94.1% 5.9% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 99% 1%
1
2
3
4
5
6
7
8
Output Classes
1
2
3
4
5
6
7
8
Target Classes
Validation1
Accuracy = 99%

## Slide 33: Support Vector Machine (SVM)(cont’d)
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 62 | 2 | 0 | 0 | 0 | 0 | 0 | 96.8% 3.2%
0 | 0 | 64 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 64 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 64 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 0 | 64 | 100% 0%
100% 0% | 100% 0% | 96.9% 3.1% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 99.4% 0.6%
1
2
3
4
5
6
7
8
Output Classes
1
2
3
4
5
6
7
8
Target Classes
Validation2
Accuracy = 99.6%

## Slide 34: Support Vector Machine (SVM)(cont’d)
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 63 | 1 | 0 | 0 | 0 | 0 | 0 | 98.4% 1.6%
0 | 0 | 64 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 64 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 64 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 0 | 64 | 100% 0%
100% 0% | 100% 0% | 98.4% 1.6% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 99.8% 0.2%
1
2
3
4
5
6
7
8
Output Classes
1
2
3
4
5
6
7
8
Target Classes
Validation3
Accuracy = 99.8%

## Slide 35: Support Vector Machine (SVM)(cont’d)
64 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 63 | 1 | 0 | 0 | 0 | 0 | 0 | 98.4% 1.6%
0 | 0 | 64 | 0 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 64 | 0 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 64 | 0 | 100% 0%
0 | 0 | 0 | 0 | 0 | 0 | 0 | 64 | 100% 0%
100% 0% | 100% 0% | 98.4% 1.6% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 100% 0% | 99.8% 0.2%
1
2
3
4
5
6
7
8
Output Classes
1
2
3
4
5
6
7
8
Target Classes
Validation4
Accuracy = 99.8%
Average Accuracy = 99.46%

## Slide 36: GMM+EM
Reference:https://www.youtube.com/watch?v=XLKoTqGao7U

## Slide 37: GMM+EM(cont’d)

## Slide 38: GMM+EM(cont’d)
validation 1: 0.9961
validation 2: 1.0
validation 3: 0.9980
validation 4: 0.9980
Total ACC : 0.9980

## Slide 39: Deep Neural Network

## Slide 40: Deep Neural Network(cont’d)

## Slide 41: Deep Neural Network(cont’d)

## Slide 42: Deep Neural Network(cont’d)
Validation accuracy 0: 0.9902343843132257
Validation accuracy 1: 0.9960937537252903
Validation accuracy 2: 1.0
Validation accuracy 3: 0.9980468768626451

## Slide 43: Deep Neural Network(cont’d)

## Slide 44: Comparison
 | SOM-MQE | SVM | GMM+EM | DNN
accuracy | 0.8809 | 0.9946 | 0.9980 | 0.9961

## Slide 45: conclusion
Time domain feature is better than frequency domain.
According to fisher criterion, entropy is the best feature to diagnosis bearing fault.
The original feature space such as entropy and variance is more distinguishable than PCA.
The GMM with EM algorithm obtain the best accuracy to determine which condition of bearing is based on the result of K-fold cross validation.

## Slide 46
Thanks for your listening